## Slide 1
Construction of Tailings Dams
Engineering Design Principles, Sequential Embankment Raising Methods, and Geotechnical Risk Management
Advanced Mining Geotechnics
Technical Monograph
ADVANCED ENGINEERING GEOLOGY — GED 452

## Slide 2
Engineering Principles
Fundamental characteristics of mining waste slurries, starter embankment foundations, and hydraulic deposition dynamics.

## Slide 3
Tailings Slurry Characteristics
Tailings consist of fine-grained mineral process residue mixed with water. Unlike water-retention dams, tailings facilities store crushed rock particles ranging from coarse sands to ultra-fine clays with variable hydraulic conductivity and liquefaction susceptibility.
Starter Embankment Structure
The initial starter dam is constructed on competent bedrock or engineered foundations using compacted rockfill or earth fill. It provides initial containment for decant pond formation and establishes the hydraulic drainage boundary for sequential raises.
Tailings & Starter Dam Design

## Slide 4
Sequential Sub-Upstream Raises
The upstream method begins with a starter dike, after which tailings slurry is spigotted along the inner crest to form a beach.
Successive dike raises are constructed directly step-wise over the previously deposited, consolidated tailings beach.
While exceptionally cost-effective and requiring minimal borrow fill, it exhibits high sensitivity to rapid raise rates, high water tables, and seismic liquefaction.
Upstream Construction Method

## Slide 5
Downstream Construction Method
High Structural Stability
Downstream dams are sequentially raised away from the impoundment, with each new raise founded entirely on compacted structural fill or coarse tailings sand downstream of the starter crest.
This design allows the inclusion of internal sand-gravel filters, low-permeability cores, and toe drain systems, rendering it resilient against extreme seismic shaking and storm events.

## Slide 6
Vertical Wall Raising
The dam axis remains constant as sequential raises are placed directly above the starter dam centerline, balancing material usage and stability.
Cyclone Sand Separation
Coarse sand fractions separated via hydrocyclones are placed on the downstream slope, while fine slime tailings flow into the upstream pond.
Moderate Seismic Resistance
Offers significantly greater resistance to static and dynamic liquefaction than upstream designs with smaller physical footprint than downstream dams.
Centerline Construction Method

## Slide 7
1.50
Minimum Factor of Safety (FoS)
Piezometric Level Control
Internal seepage management is the single most critical factor in slope stability. The phreatic line must be kept deep within the embankment shell.
High pore-water pressures reduce effective normal stress along potential slip surfaces, leading to slope failure or piping erosion. Basal blanket drains and chimney drains are installed to safely discharge seepage water.
Phreatic Surface & Seepage

## Slide 8
Vibrating Wire Piezometers: Installed at multiple vertical and horizontal grid points to provide real-time monitoring of internal pore water pressures and water table elevations.
Inclinometers & Extensometers: Measure lateral subsurface deformation and settlement within the embankment zones to detect early creep or shearing signs.
InSAR & GNSS Automated Surveys: Millimeter-accurate satellite radar interferometry and continuous GPS station arrays track surface movement across the entire impoundment.
Seepage Flow Weirs: V-notch flumes measure turbidity and volumetric flow rate of drained water to verify filter integrity and catch piping piping early.
Instrumentation & Monitoring

## Slide 9
Design Criterion | Upstream Method | Centerline Method | Downstream Method
Fill Volume Needed | Very Low (Most Economical) | Moderate | High (Largest Footprint)
Seismic Liquefaction Risk | High / Vulnerable | Moderate Resistance | Very Low / High Resistance
Water Storage Capacity | Poor (Requires wide beach) | Fair | Excellent (Can retain pond)
Rate of Raise Constraint | Slow (Requires drying time) | Moderate | Flexible / Fast
Regulatory Acceptance | Banned in many jurisdictions | Conditional Approval | Widely Accepted Globally
Comparison of Raise Methods

## Slide 10
Filtered / Dry Stack
Mechanical vacuum or pressure filtration reduces moisture content below 20%, allowing non-slurry dry stacking without retaining dams.
Thickened / Paste Tailings
High-rate thickeners dewater slurries to a non-segregating paste consistency, reducing free water and footprint area.
In-Pit Backfilling
Deposition directly into exhausted open pit voids or underground stopes, eliminating surface dam structures entirely.
Alternative Tailings Storage

## Slide 11
Stability & Seismic Safety

## Slide 12
Questions & Discussion
Global Industry Standard on Tailings Management (GTRM) Compliance & Best Practices

## Slide 13
https://www.tailings.info/images/assets/content/upstream.jpg
Source: www.tailings.info
https://live.staticflickr.com/4538/24553044818_4fd925ee56_o.jpg
Source: www.grida.no
https://www.tailings.info/images/assets/content/bigdrystack.jpg
Source: www.tailings.info
https://www.westechwater.com/hs-fs/hubfs/image/page/case-study/hidensity-paste-thickener-paragominas-brazil/hidensity-paste-thickener-at-paragominas-brazil-768w.jpg?noresize&width=768&height=480&name=hidensity-paste-thickener-at-paragominas-brazil-768w.jpg
Source: www.westechwater.com
https://www.mdpi.com/minerals/minerals-11-00818/article_deploy/html/images/minerals-11-00818-g001-550.jpg
Source: www.mdpi.com
Image Sources